B-> D* K for superB
B->D(*)K, are main processes to measure 3 angle
D->Ks Dalitz, D->K ADS, D->fCP GLW methods are used.
The efficiency and background ratio is very important for D* modes: D*0-> D00, D0
The efficiency is checked for 3 detector sets: current, pure CsI endcaps and intermediate: pure CsI for cID 1-480, 8449-8736.
x4 background of exp.49 is used.
The efficiency is compared with x1 background case.
The background in pure CsI is assumed to be x1.

---
Gamma require width < 6
Mdst gamma require width<6
For x4 bckg about 50% are cuted
X4 Bckg
X1 bckg

---
0 mass
Old selection
Remove <6 cut

---
Efficiency degradation with x4 backround
Efficiency for low energy gammas and pi0 is decreasing by ~20% with x4 beam background. Using of pure CsI for endcups allow to improve the efficiency by ~10%
81%
93%
pureCsI
76%
90%
half pureCsI
73%
86%
Current setup
D0
D00
Efficiency

---
Background estimation
Background estimation
Background is estimated using 2M BBar generic MC sample. The statistics is not enough find a dependence from ECL bkg level.
We consider the same background level as for x1 luminosity

---
Walidity of MC
Fraction of the events B->D*K, D*->D0 is 3 0%
Geometricaly it should be about 40%
There is thick passive material in front of the endcaps in Belle(both in X0 and geometricaly)
sBelle PID is (planed) to be thinner.

---
Conclusion
Slow 0 efficiency significantly decrease with high background.
The use of pure CsI can improve the efficiency by 10%.
We need more generic MC to estimate the background level
We need to make MC with realistic detector description (dead material in front of CsI)