## Slide 1: Prototype batch of DSSD from commercial vendors & Proposal for SVD Layout
18 March 2009
Thomas Bergauer
HEPHY Vienna

## Slide 2: Conclusion from 6” DSSD market survey
High throughput (100 wafers per month)
  Micron
  SINTEF
Mid-size throughput (30 wafers per month)
  Canberra
Hamamatsu?
  Not yet clear if they will decide to re-start DSSD production
  Even if they do: It will be probably too late (at least for R&D)
Thomas Bergauer
18 March 2009
[presented in last upgrade meeting (Dec 08)]

## Slide 3: Question for quotation
I have contacted both, Micron and SINTEF to get a quotation for 20-30 pcs DSSD
Specifications:
6” DSSD 300 micron thickness to accommodate one main sensor with 12x4 cm
768 strips on each side with 50 (p-) and 150 micron (n-side)
Poly-Silicon biasing > 5 MOhm
Coupling Capacitance larger than 1.2 pF per cm (strip length) and per um (strip width) dielectric
number of pinholes per sensor: < 0.5%
total leakage current <10uA at 1.5*V_depletion at 21 C
Minimum breakthrough voltage >2.5*V_depletion
Thomas Bergauer
18 March 2009

## Slide 4: Answers received
I have received answers from both companies:
SINTEF
  active communication between me and the senior physicist to clarify several technical aspects
  Lengthy quotation with all technical details, detailed payment and delivery scheme
Micron
  No communication with them until I have received an email with the quotation. No discussion about technical details.
  However, I met their director at TIPP09 conference and discussed with him a bit.
Thomas Bergauer
18 March 2009

## Slide 5: Comparison of the two Quotations
 | SINTEF | Micron
N-type FZ bulk material | 3.5-12 kOhm cm, <100>, not in stock (Topsil) | 8kOhm cm, <100>, in stock (Topsil+ etching and polishing @ external company)
Thickness | 300 um +/- 25um | 300um +/-5 um
Full depletion voltage | max. 90V | 40V (according to resistivity)
Poly-Si bias resistor | 5-100 MOhm (typically 10 MOhm) | 10 (+/- 5) MOhm
Strip Isolation | P-stop | P-stop
Masks | 14 pcs. 7x7 inch (Photronics), with working copies | 15 pcs. 7x7 inch (Photronics), master only
Number of bad strips | 10 (per side) | 38 per side (first 10 pcs.) 7 per side (remaining 20 pcs)
Thomas Bergauer
18 March 2009

## Slide 6: Lead time comparison
 | SINTEF | Micron
Commencing |  | 6 months
Wafer Procurement | 10 weeks | -
Completion | 30 weeks=7.5 months | 9 months
Contingency | +/- 1 month | +/- 1 month
Quotation Validity | 30 days | End of December 2009
Thomas Bergauer
18 March 2009

## Slide 7: Cost Comparison
 | SINTEF | Micron
Masks | 5.5 M¥ | 4.4 M¥
Probe card + Test setup | 0.9 M¥ | 0.3 M¥
Testing, Packaging | 1.6 M¥ | 0.4 M¥
Administration | 1.6 M¥ | -
Review and adaptation of photo mask | 25 k¥ per hour (not included in sum!) | -
Processing | 13 M¥ (23 pcs) | 2.5 M¥ (first 10 pcs.) 5 M¥ (next 20pcs.)
Total Sum | 22.5 M¥ (178 k€) | 15 M¥ (120 k€)
Sensors received | 23 | 30
Cost per sensor | ~1 M¥ (8k €) | ~0.5 M¥ (4k €)
Thomas Bergauer
18 March 2009

## Slide 8: Comments
Pro/Cons
  SINTEF is much more expensive than Micron (twice as much!)
  SINTEF takes everything more seriously
  Micron has only 1 person for each job
Maybe we should consider also to contact Canberra for a quotation, to check if Micron’s price is low or SINTEF’s numbers are too high
If Hamamatsu is really re-starting DSSD production in the future we should anyhow go with Micron for a prototype batch now for R&D (e.g. Origami concept)
However: The total number of sensors for the new SVD is not so high that HPK will do so only for us.
Thomas Bergauer
18 March 2009

## Slide 9: What would we do with 6” DSSD?
We will learn about the quality an reliability of the chosen producer - if it is Micron, SINTEF or another
We will produce a ladder of Origami modules to be tested in a testbeam under real conditions to get S/N results comparable to real future SVD case
Thomas Bergauer
18 March 2009

## Slide 10: PROPOSAL FOR SVD LAYOUT
and cost estimate
Thomas Bergauer & Markus Friedl
18 March 2009

## Slide 11: Design Considerations
Design driven by
  Geometry of 6” silicon sensors
  Material budget (hybrids outside acceptance region)
  No Origami modules in layer 3
  Minimum number of sensor designs
Outermost layer 6 given by CDC inner radius
Layer 5 given by simulation from Hara-san
  2 cm inside outermost layer
Thomas Bergauer
18 March 2009

## Slide 12: Proposed 6” SVD Layer Arrangement
18 March 2009
15 deg
20 deg
20 deg
Layer | Radius (barrel) | Radius (slanted)
6 | 14 cm | 10.7 – 14 cm
5 | 12 cm | 8.3 – 12 cm
4 | 9 cm | 6.1 – 9 cm
3 | 4.5 cm | -
Thomas Bergauer & Markus Friedl

## Slide 13: SVD Layout with 2 sensor types only
18 March 2009
Thomas Bergauer & Markus Friedl

## Slide 14: SVD Layout with 2 sensor types only
Layer | # Ladders | Rectangular Sensors | Wedge Sensors | APVs
6 | 24 | 96 | 24 | 1392
5 | 24 | 72 | 24 | 1104
4 | 16 | 32 | 16 | 544
3 | 8 | 16 | 0 | 192
Sum: | 72 | 216 | 64 | 3232
Unit Cost: |  | 2k€ | 2k€ | 400€ *)
NRE Cost: |  | 40k€ | 40k€ | 
Total Cost: |  | 472k€ | 168k€ | 1293k€
Total: |  |  |  | 1933k€ (2.5 oku¥)
18 March 2009
*) 400 € per APV includes readout electronics, but not power supplies
Thomas Bergauer & Markus Friedl

## Slide 15: APV costs (preliminary guess)
Include costs of full readout chain
Does not include
  power supplies
  COPPER/Finesse
Numbers from SVD3
Parts for readout | Cost
16 APV chips | 0.32 k€
FADC | 3k€
REBO+MAMBO | 1.1k€
cables | 0.1k€
Part of VME crate, rack | 1k
Sum | 5.5 k€
Multiplicity APV/board | 16
Cost per APV | 345 €
Total sum including contingency (preliminary guess) | 400 €
18 March 2009
Thomas Bergauer & Markus Friedl

## Slide 16: SVD Layout with 3 sensor types
18 March 2009
Thomas Bergauer & Markus Friedl

## Slide 17: SVD Layout with 3 sensor types
18 March 2009
Layer | # Ladders | Rect. Sensors [50μm] | Rect. Sensors [75μm] | Wedge Sensors | APVs
6 | 24 | 0 | 96 | 24 | 960
5 | 24 | 0 | 72 | 24 | 768
4 | 16 | 32 | 0 | 16 | 544
3 | 8 | 16 | 0 | 0 | 192
Sum: | 72 | 48 | 168 | 64 | 2464
Unit Cost: |  | 2k€ | 2k€ | 2k€ | 400€
NRE Cost: |  | 40k€ | 40k€ | 40k€ | 
Total Cost: |  | 136k€ | 376k€ | 168k€ | 986k€
Total: |  |  |  |  | 1666k€ (2.1 oku¥)
Thomas Bergauer & Markus Friedl

## Slide 18: Summary Costs
 | 2-layout design | 3-layout design
Rectangular (50/160μm pitch) | 216 | 48
Rectangular (75/240μm pitch) | - | 168
Wedge-shaped (50-75/160μm pitch) | 64 | -
Wedge-shaped (50-75/240μm pitch) | - | 64
Sum: | 280 | 280
Total active area: | 1.27 m2 | 1.27 m2
Total sensor costs (Micron): | 640 k€ | 680 k€
Number of APVs | 3232 | 2464
Total SVD costs: (excluding power supplies) | 1933k€ (2.5 oku¥) | 1666k€ (2.1 oku¥)
18 March 2009
Thomas Bergauer & Markus Friedl

## Slide 19: Comments
Calculation is very preliminary
It contains
  Full APV readout chain
  NO power supplies and NO COPPER/Finesse
  Costs of silicon sensors based on Micron quotation (WITHOUT any spares and prototypes)
If we want to go to with SINTEF, sensor price will be almost doubled
HPK will probably not re-start DSSD production for such a small number of sensors
18 March 2009
Thomas Bergauer & Markus Friedl