## Slide 1: CDC readout system status
MT 2009 July 7

## Slide 2: BELLE II
CDC readout electronics
CDC

## Slide 3: Prototype CDC readout card (FY2009)
# of channels(Total:～15000)
  48～64ch/board
Amp shaper
  Shaping time:～100nsec
  Gain:～1V/1pC（TBD)
  Dynamic range:2pC（TBD)
TDC  FPGA TDC
  Timing resolution:1nsec
ADC
  Resolution:10bit
  Sampling rate:～32MHz
L1 buffer
  Depth:5usec max
Test board was developed to determine above params
using test chamber.

## Slide 4
Test board for test(prototype readout card will be designed based on this.)
Small tube chamber (tungsten wire)
Fe55 5.9 keV X-ray
Gas(Ar90%+CH410%), P10 Gas
1.65kV
16ch
Ampshaper
AD9212x2
TDC&L1 buf
RocketIO
RMS=0.47ns
This AmpShaper was developed for other application.
Modification will be done by Dr. Taniguchi.
FPGA-TDC has been used for J-PARC.
Firmware design will be done by Dr.Uchida
PCB was designed by Mr. Saito and Mr. Ikeno
RocketIO will be tested by Dr. Igarashi

## Slide 5: Specification of Test board(detail)
Analog(Amp-shaper for DB-decay exp)
  Peaking time:～50nsec  OK
  Pulse width:～200nsec  OK
  Gain : 8V/pC  1～２V/pC
  Dynamic range : 2V max  OK
  Noise : ～2500 e @ 40pF  OK
Function
  ADC 10bit 32MHz
  TDC 1nsec
  L1 buffer : 5usec max
  Two modes for data format
    Waveform data readout mode
    Compression mode Timing and Q
These values will be confirmed by beam test
BLR modification has been done

## Slide 6: Amp shaper modification
CMOS digital
BLR
Analog buffer
Amp shaper
Bias circuit
Present Amp shaper
We started development of Amp-shaper for BELLEII CDC.

## Slide 7: FPGA Block diagram
FADC I/F
ADC
TDC
ASD
Ring buffer
5usec
500nsec window
Readout
FIFO
Q(sum)
&
Data formatter
SiTCP
Or
RocketIO
I/F
Slow control
DAC, ADC, Ring buffer etc
Trigger

## Slide 8: Function
L1 buffer length : 5usec Max variable
New
old
Trigger
Window(for Q info:S) 500nsec variable
Timing data and Q or waveform data are
Transferred to external interface
ADC waveform
Comparator output
Data format will be determined within a month

## Slide 9: Schedule(short term)
Firmware
w/o rocket IO
End of Aug.
prototyping
modification
End of Sept.
Preparation for beamtest
Amp shaper
Mid of Oct.
Design and feedback
submission
Test with rocket IO
PCB design
Uchida
Taniguchi, Shimazaki
Nakao, Igarashi
Saito, Ikeno